## Slide 1
CMP3010: Computer Architecture
Pipelining Hazards
Mayada Hadhoud
Computer Engineering Department
Cairo University
Notes: 1

## Slide 2
Agenda
Pipelining Hazards
Structural Hazards
  Structural Hazards Solutions
Data Hazards
  Data Hazards Solutions
Control Hazards
  Control Hazards Solutions
Exceptions

## Slide 3
Question??
Assume
  Fetch = 10 ns
  Decode = 6 ns
  Execute = 8 ns
  Memory = 10 ns
  Write back = 6 ns
What is the speedup of a pipelined processor Vs. Single cycle processor and Multi cycle processor ?
Given : Number of instructions is 1000 instruction (50% add and sub instructions, 10% load , 10% store, 30% branch)
Notes: Single cycle:
40 ns cycle time
Total time = 1000x 40=40000ns
Multi cycle:
Cycle time=10ns
Add/sub:4 cycles
Load:5 cycles
Store:4 cycles
Branch:3 cycles
Total time=600x40+100x50+300x30=24000+5000+9000=38000
Pipeline:
Cycle time= 10 ns
Total time= 1000x10+40=10040ns
Speed up single=4
Speed up multi = 3.8
3

## Slide 4
Pipeline Hazards
Hazards: Situations that prevent an instruction from being executed in its designated clock cycle
Types of Hazards
  Structural Hazards: two different instructions use same h/w in same cycle
  Data Hazards: An instruction depends on the results of previous instruction
  Control Hazards: When an instruction changes PC, like branches
The simplest hazards solution is to stall the pipeline (some instructions are allowed to proceed, while other are delayed)

## Slide 5
Structural hazards
No two instructions are processed by the same module at the same time.
Solutions:
  Stalling the pipeline (inserting bubbles)
  Hardware Duplication

## Slide 6
Structural hazards
Examples
  Instruction fetch is conflicting with data memory access
    Use two separate caches one for instructions and one for the data.
  Register file is accessed by the instruction in the decode (reading) and the instruction in the write-back (writing)
    Ensure that writing is done in the first half of the clock and reading is done at the second half of the clock

## Slide 7
Appendix A - Pipelining
7
Structural Hazards
When two or more different instructions want to use same hardware resource in same cycle
e.g., MEM uses the same memory port as IF as shown in this slide.
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Instr 3
Instr 4
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg
Notes: 7

## Slide 8
8
Structural Hazards
This is another way of looking at the effect of a stall.
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Stall
Instr 3
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg
Bubble
Bubble
Bubble
Bubble
Bubble
Notes: 8

## Slide 9
Data Hazards
An occurrence in which a planned instruction cannot execute in the proper clock cycle because data that is needed to execute the instruction is not yet available.

## Slide 10
Data Hazards
Data hazards arise from the dependence of one instruction on an earlier one that is still in the pipeline.
Example:

## Slide 11
Example
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)
IF
ID/RF
EX
MEM
WB
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 12
Data Hazards- Solutions
Solution (1): Software-solution: Compiler arranges instructions to avoid data dependencies
Solution (2): Data Forwarding “or bypassing”: forward the data back to the requesting stage “immediately when it is available”
Solution (3): Stalling the pipeline: inserting bubbles and stall the instruction till the data is written back

## Slide 13
Data Forwarding

## Slide 14
Data Forwarding

## Slide 16
16
HW Change for Forwarding
MEM/WR
ID/EX
EX/MEM
Data
Memory
ALU
mux
mux
Registers
NextPC
Immediate
mux

## Slide 17
Notes: 1. EX hazard:
if (EX/MEM.RegWrite and (EX/MEM.RegisterRd 0)
and (EX/MEM.RegisterRd = ID/EX.RegisterRs)) ForwardA = 10
if (EX/MEM.RegWrite and (EX/MEM.RegisterRd 0)
and (EX/MEM.RegisterRd = ID/EX.RegisterRt)) ForwardB = 10
2. MEM hazard:
if (MEM/WB.RegWrite and (MEM/WB.RegisterRd 0)
and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
if (MEM/WB.RegWrite and (MEM/WB.RegisterRd 0)
and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01
if (MEM/WB.RegWrite and (MEM/WB.RegisterRd 0) and (EX/MEM.RegisterRd ID/EX.RegisterRs)
and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
if (MEM/WB.RegWrite and (MEM/WB.RegisterRd 0) and (EX/MEM.RegisterRd ID/EX.RegisterRt)
and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01
17

## Slide 18
Load-Use Data Hazard
A specific form of data hazard in which the data requested by a load instruction has not yet become available when it is requested.

## Slide 19
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
or r8,r1,r9
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 20
Try producing fast code for
a = b + c;
d = e – f;
assuming a, b, c, d ,e, and f in memory.
Slow code:
LW Rb,b
LW Rc,c
ADD Ra,Rb,Rc
SW a,Ra
LW Re,e
LW Rf,f
SUB Rd,Re,Rf
SW d,Rd
Software Scheduling to Avoid Load Hazards
Fast code:
LW Rb,b
LW Rc,c
LW Re,e
ADD Ra,Rb,Rc
LW Rf,f
SW a,Ra
SUB Rd,Re,Rf
SW d,Rd

## Slide 21
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
Reg
ALU
DMem
Ifetch
Reg
Reg
Ifetch
ALU
DMem
Reg
Bubble
Ifetch
ALU
DMem
Reg
Bubble
Reg
Ifetch
ALU
DMem
Bubble
Reg
Pipeline should be stalled till the data becomes available

## Slide 22
Load-Use Data Hazard

## Slide 23
Load-Use Data Hazard
Load-Use Hazard check
Is the instruction is load ??
How can we insert NOP in the pipe??
Notes: NOP: changing the EX, MEM, and WB control fields of the ID/EX pipeline register to 0. an it will propagate to the next registers
23

## Slide 24
Data Hazard Detection H/W