## Slide 1: VLSI Lab 2
Cairo University
Faculty of Engineering
Computer Engineering Department
Sandra Wahid

## Slide 2
TCL

## Slide 3: TCL
Tcl (Tool Command Language)
Tcl scripts are made up of commands separated by newlines or semicolons.
Commands all have the same basic form.
  Each Tcl command consists of one or more words separated by spaces.
Example:
  expr 20 + 10
  This command computes the sum of 20 and 10 and returns the result, 30.

## Slide 4: TCL
The set command is used to write and read variables.
  set x 32 //x=32
  set x //reads x value
To use the value of a variable in a command, use variable substitution as in the following example:
  expr $x*3
You can use variable substitution in any word of any command, or even multiple times within a word.

## Slide 5: TCL
When a [ appears in a command, Tcl treats everything between it and the matching ] as a nested Tcl command.
  Tcl evaluates the nested command and substitutes its result into the enclosing command in place of the bracketed text.
  Example:
  set a 44
  set b [expr $a*4]

## Slide 6: Note
If while executing a file, you got the error:
“Permission denied” then use the following
command (grant execution permission):
chmod +x filename.extension

## Slide 7
Synthesis

## Slide 8: Synthesis
High-level design descriptions written in Hardware Description Languages (such as VHDL, Verilog)
Gate-Level Netlist
Gate-level netlist is basically a circuit implementation of the design made of library components (both combinational and sequential cells) available in the technology library and their interconnections.
The netlist is generated by the synthesis tool according to the constraints set by the designer.

## Slide 9: Synthesis
Synthesis takes place in multiple steps:
  Converting RTL into simple logic gates.
  Mapping those gates to actual technology-dependent logic gates available in the technology libraries.
  Optimizing the mapped netlist keeping the constraints set by the designer intact.

## Slide 10: Design Tradeoffs
System Physics:
System Requirements:
  Frequency
  Chip Area
  Power Consumption
As the Area of the design increases  the number of transistors increase & the capacitance increase.
Application Specific designs are compared using Power/Area or Power/Throughput
P α C⋅V2⋅f
Power α Capacitance * Voltage2 * Frequency
C α Area

## Slide 11
Synthesis
Oasys-RTL

## Slide 12: Read Libraries
Technology Files (.lib)Liberty Timing File
  describe Timing constraints for each cell (Capacitance, resistances, rise and fall delays ..etc)
  Command: read_library
Physical libraries (.lef) Library Exchange Format
  describe the cells as shapes (width, height and antennas effect, vias places and metals, …etc)
  Command: read_lef
Process technology ( .ptf)Process Technology File
  used for layer parasitic extraction, e.g.: when two conductive elements are close to each other and at different voltage levels they form an unwanted capacitor. This is known as the parasitic capacitive effect.
  Command: read_ptf
Power files (.upf)Unified Power Format
  describe which power rails should be routed to individual blocks, when blocks are expected to be powered up or shut down, how voltage levels should be shifted as signals cross from one power domain to another
  Command: load_upf

## Slide 13: Read RTL
Verilog or VHDL design.
  Command:
    Verilog: read_verilog “file1.v file2.v”
    VHDL: read_vhdl “file1.vhd file2.vhd”

## Slide 14: Make Synthesis-Specific Settings (Optional)
Set the max number of routing layers to use in physical optimization
  Command:
  set_max_route_layer 5
Reset don’t use property on all lib cells (to use all of them)
  Command:
  set_dont_use [get_lib_cell *] false
Set clock gating options
  Command:
  set_clock_gating_options
  –minimum_bitwidth 4
  –sequential_cell latch
Notes: minimum_bitwidth : Specifies the minimum number of flip-flops that share common enable logic for the flip-flops to be clock-gated. The <bitwidth> value must be an integer. If this option is not specified, the default is 4.
sequential_cell : Specifies the type of sequential element to use for the clock_gating_integrated_cell.

## Slide 15: Note
Any command you want to know its usage, arguments, description and examples:
  man
  E.g.: man set_max_route_layer
Any command you want to know its arguments:
  help
  E.g.: set_max_route_layer -help

## Slide 16: Note
Example from oasys:

## Slide 17: Synthesize
Synthesize
  Command:
  synthesize –module ${top_module_name}
Save in a format friendly to Oasys-RTL
  Command:
  write_design ${output_dir}/synthesized_example.odb

## Slide 18: Constraints
Read timing constraints
  Command:
  read_sdc StandardDelayConstraints.sdc
  E.g.: clk period, signal transition time
  #optional
  read_def floorplanningtimingConstraints.fp.sdc
Create Area constraints #optional
  Command:
  create_chip -util 0.70 -aspect_ratio 0.8
  -utilization <percentage>
  Required if neither the -height and -width argument pair nor the -points argument is used. Specifies the chip utilization as a percentage of the die area. If you have problems with routing congestion, reducing this value should reduce the congestion.
  The chip utilization is based on the total cell area, which includes all the standard cells, macros, I/O pads, and physical-only cells.
  Chip Utilization = Total Cell Area / Die Area
  -aspect_ratio <ratio>
  Optional. Specifies the ratio of the height and width of the chip. The default is 1. The -height, -width, and -points options override -aspect_ratio.

## Slide 19: Optimize
Optimize for timing
  Command: optimize –virtual
Optimize for placement
  Command: optimize –place
OR just optimize
  Command: optimize
Save in a format friendly to Oasys-RTL after each optimize
  Command: write_design ${output_dir}/optimized_time_example.odb

## Slide 20: Output and Analysis
Reports: you can generate several reports and save them to files for further investigation
  report_units
    Outputs the SDC units for time, capacitance, resistance, power, voltage, and current.
  report_timing > ${log_dir}/time.rpt
    Reports the worst paths (based on slack) in the design that satisfies the given constraints.
    Slack:
      It is difference between the desired arrival times and the actual arrival time for a signal.
      Slack time determines [for a timing path], if the design is working at the desired frequency.
      Positive Slack indicates that the design is meeting the timing and still it can be improved.
      Zero slack means that the design is critically working at the desired frequency.
      Negative slack means , design has not achieved the specified timings at the specified frequency.
      Slack has to be positive always and negative slack indicates a violation in timing.

## Slide 21: Output and Analysis
  report_endpoints > ${log_dir}/endpoints.rpt
    Reports the worst endpoints and their slacks, sorted by criticality.
  report_design_metrics > ${log_dir}/design_metrics.rpt
    Reports the design characteristics of the top-level design in the session. Design size, power, instance count, physical data including die size, and congestion are reported.
  report_path_groups > ${log_dir}/paths.rpt
    Reports quantitative information about each existing path group.
  report_power > ${log_dir}/power.rpt
    Reports the power consumption information for the design.

## Slide 22: Output and Analysis
Outputs:
  To continue with Nitro-SoC only MXDB is needed
  Other files are needed to use non-mentor tools or to perform Post-synthesis simulation
Write in Oasys internal format
  write_design ${out_dir}/example.odb
Write MXDB
  write_mxdb ${out_dir}/example.mxdb
Write netlist in Verilog
  write_verilog ${out_dir}/out_example.v
Write time constraints
  write_sdc ${out_dir}/out_time.sdc
Write floorplan
  write_def –floorplan ${out_dir}/out_example.def
Save UPF commands in the design to a file
  save_upf ${out_dir}/out_upf.upf

## Slide 23: Folders Hierarchy
lib_data: libraries (.lib, .lef, .ptf)
rtl: your design (.v or .vhd)
constraints: power files (.upf) and constraints (.sdc)
scripts: tcl with commands
output: folders for different outputs

## Slide 24: Scripts
0_init_design.tcl
1_read_design.tcl
2_synthesize_optimize.tcl
3_export_design.tcl
run.tcl: script to run (runs scripts 03)
cleanup.sh: to restart the flow again
  [vlsi@localhost ~]$ ./cleanup.sh
  [vlsi@localhost ~]$ oasys
  [oasys-RTL]$ source scripts/run.tcl

## Slide 25: Scripts
Generally, we need to change the following:
  In “0_init_design.tcl”:
    set top_module "carry_lookahead_adder“
    set rtl_list { CLA_generic.v full_adder.v }
    Any changed libraries or constraints
  In “1_read_design.tcl”:
    Only if changed Verilog or Vhdl:
    read_verilog $rtl_list -include $search_path

## Slide 26: Design Schematic
  [vlsi@localhost ~]$ oasys –gui
  From Design tab  run.tcl
  From Netlist tab: double click on each component to get the final design schematic
  Zoom In

## Slide 27
Example

## Slide 28: Example: carry_lookahead_adder
The difference is that carry lookahead adders are able to calculate the Carry bit before the Full Adder is done with its operation.

## Slide 29: Example: carry_lookahead_adder

## Slide 30: Example: carry_lookahead_adder
demo_adder.syn.v
  Contains netlist
    a netlist is a description of the connectivity of an electronic circuit.
    We have 77 instances from 0 to 76

## Slide 31: Example: carry_lookahead_adder
design.rpt:
Utilization= Movable Cell Area/Placeable Area
Chip Area is not fully used  we can only use Placeable Area after removing “blockage for IO’s” from Chip Area
Utilization must not be very high (max. 70-80%) as there is still routing

## Slide 32: Example: carry_lookahead_adder
power.rpt:

## Slide 33: Example: carry_lookahead_adder
endpoints.rpt:

## Slide 34: Example: carry_lookahead_adder
path.rpt:
Worst is the least slack

## Slide 35
Thank You